11.1
- I found a paper about resonant charge exchange & elastic cross section in O2 and N2. I still need to find: 1. resonant of O+ 2. dissociative charge transfer (ion-molecule) 3. coulomb collision 4. elastic scattering between diff species, and O

Tasks to do
1. look into neutral beam source with gas charge exchange neutralization in other applications
2. look into how to maintain a pressure difference in vacuum chamber
3. figure out the mechanism to produce O from O2
4. O+/O2 cross section is approx. 2e-16 cm^2 for ground state, and 3e-15 cm^2 for metastable ions. (why the difference? what is metastable?)
5. What is the benefit of such scheme compared with existing VLEO simulator, eg. RF quasi-neutral plasma, RIT?

Excitation is when an orbiting electron moves to higher orbit due to energy input. Potential energy increases.

Trade-offs of gas cell approach:
When comparing with a plasma / EP thruster type source:
Pros:
1. True neutral atom beam instead of quasi-neutral (electron + ion flow)
2. No electron contamination
3. Characterize erosion through AO
Cons:
1. Complexity & cost resulted from a) ion stage + gas cell + ion deflector b) vacuum isolation c) cryogenic cooling for gas injection; whereas an EP neutral source can reuse the actual ABEP thruster design (eg. the same RIT)
2. Low efficiency: 31% conversion rate (a case study), and hence limited flux

When comparing with surface neutralization:

Challenge:
1. No study on CEX with a mixed gas (at 200km, 58%O 41%N 1%O2)

An electrodeless source cause spread in VDF, causing multiple ion energy spikes (not good), eg.